## Slide 1
VECTO 2.1 20.04.2015
Release Notes

## Slide 2
VECTO 2.1
New AT/TC options:
  Limit engine rpm in torque converter operation acc. ≥ accmin
  Shift up (C-to-L, L-to-L) if acc. ≥ accmin and next-gear-rpm > threshold
  rpm limit [1/min] and accmin [m/s²] parameters are currently user-defined
  C-to-C up-shift condition based on N80h engine speed (instead of N95h)
Pwheel input (SiCo test mode)
  Pwheel as cycle input
  Overwrites power calculation
  VECTO only calculates power train losses, engine torque/rpm and fuel consumption

## Slide 3
"Test" tab in main form includes new parameters.
Note: This is a temporary solution until model and parameters are verified!
AT/TC model update

## Slide 4
New AT/TC paramters:
  TClimitOn (True / False)
    Enables engine rpm limit in TC operation
  TClimit [1/min]
    engine rpm limit (if TClimitOn = True)
  TCshiftMode (0/1)
    Mode 0: acc_target - Shift up if power demand with target acc. < power-max (pre-V2.1 default)
    Mode 1: acc_min - Shift up if power demand with min. acc. < power-max
  TCaccMin [m/s²]
    Minimum acceleration for ShiftMode 1 and TClimit
Note: This is a temporary solution until model and parameters are verified!
AT/TC model update

## Slide 5
AT/TC model update
Change parameters in Test tab by double-click
Parameters are saved on application level (..\config\DEVconfig.txt)
Note: This is a temporary solution until model and parameters are verified!

## Slide 6
Pwheel can be defined in driving cycle to overwrite power calculation
Requires Gear and Engine Speed input
Cycle identifier: <Pwheel>
Only distance-based cycles are supported
Distance Correction must be disabled (Options tab in main form)
Pwheel Input (SiCo Mode)
Example driving cycle

## Slide 7: Full Changelog V2.1
Limit engine rpm in torque converter operation acc. > acc_min
Shift up (C-to-L, L-to-L) if acc. > acc_min and next-gear-rpm > threshold
C-to-C up-shift condition based on N80h engine speed (instead of N95h)
Pwheel-Input (SiCo Mode)
FC [g/h] is always saved in output (in addition to [g/km]), not only in Engine Only mode
GUI: Corrected air density unit in GUI
Bugfix: Format error in .vmod header
VECTO 2.0.4-beta4_Test (Test Release)
Transmission loss extrapolation Errors are now Warnings in Engineering Mode.
Bugfix: Error in TC Iteration caused crash
Bugfix: Minimizing Graph window caused crash
Fixed error in cycle conversion
Errors if full load curve is too "short"
Changelog since version 2.0.4-beta3. For full changelog see VECTO Main Form > Help > User Manual
or CITnet.