## Slide 1
VECTO 1.4
07.10.2013
Update Notes

## Slide 2
Update Overview:
Eco-Roll and Look-Ahead Coasting revised
Major update in Gearbox/Toque Converter
Engine Only Mode: Engine motoring points can be defined explicitly in load cycle
Full load and drag curves (.vfld) can be defined for each gear separately
Load-dependent rolling resistance coefficients
Start-Stop activation delay time can be defined in job file
File signing features added
Various bug fixes and optimisations
VECTO 1.4

## Slide 3
Eco Roll
New rules for Eco Roll (de-)activation:
Activation if Pwheel* < 0
Deactivation if Underspeed is reached
* Pwheel = Total power demand at wheels
Eco Roll activated
Pwheel<0
Eco Roll deactivated
Underspeed
reached

## Slide 4
Look-Ahead Coasting
Real coasting also if road gradient > 0
  Deceleration may be so high that no braking is necessary. In this case the braking phase will be omitted. (Before V1.4 coasting was not affected by road gradient, if > 0)
Distance Correction now also affects coasting phases
  Lower distance error
  Coasting phases may be interrupted temporary to correct distance. (To be revised in future updates)

## Slide 5
Gearbox & Toque Converter
Torque converter can now be defined in multiple gears
Double-click to edit gear
Note: Old Gearbox files (V1.3.1) are compatible with V1.4

## Slide 6
Gear 1 = First mechanical gear with TC active*
Gear 2 = Second mechanical gear with TC active
Gear 3 = Second mechanical gear with TC inactive
Gearbox & Toque Converter
Example: Torque converter active in first and second gear
* TC active = lock-up clutch open
Gear 2 and 3 are the same mechanical gear (same gear ratio)
Note: Gear numbers in results are the same as here (i.e. no more "0.5" gear)!

## Slide 7
Toque Converter Setup
Conventional Automatic Transmission
Torque converter file is defined for torque converter only
Define TC gear with ratio of first (mechanical) gear
Set transmission losses of first gear (map or constant efficiency)
Engine
TC
Speed Ratio ν = nout / nin
Torque Ratio μ = Tout / Tin
MP1000
nin, Tin
nout, Tout
Torque Converter file (.vtcc)
Gearbox Out
= Gearbox In

## Slide 8
Power-distributed Automatic Transmission
Torque converter file is defined for the whole gearbox
Define TC gear with ratio = 1
Set transmission efficiency to 1 (= 100%) because losses are covered by .vtcc file
Toque Converter Setup
Engine
Speed Ratio ν = nout / nin
Torque Ratio μ = Tout / Tin
MP1000
nin, Tin
nout, Tout
TC
Torque Converter file (.vtcc)
= Gearbox Out
= Gearbox In

## Slide 9
Gearbox & Toque Converter
More changes:
Same gear numbers in output as in GBX file, i.e. first gear with TC is not "TC" or "0.5" but simply "1"
"Minimum time between two gear shifts" now also limits torque converter shifts
Unlimited number of gears and new gear list in GUI without fixed gear number
Improved gear shift model for torque converter
Driving Cycle Preprocessing and Gear Shift Model now use approximated efficiency values based in the transmission loss maps.
  Reduces calculation time significantly with little to no impact on fuel consumption.

## Slide 10
Motoring in Engine Only Mode
Engine motoring points can be defined explicitly in load cycle by using the <DRAG> keyword
Load cycle (.vdri)
Engine Speed
Engine Torque
Drag Torque from .vfld file

## Slide 11
Gear-dependent full load curves
Double-click to edit
Each .vfld file can be assigned to a single gear or a range of gears
Note: Old Engine files (V1.3.1) are compatible with V1.4

## Slide 12
Load-dependent rolling resistance coefficient
For each axle the RRC* and test load Fz* are defined
Double-click to edit axle config.
Relative axle load s(i)
(share of total weight)
RRCISO(i)*
* according to ISO 28580 (Test load: 85% of max. load capacity)
FzISO(i)*
Twin Tyres => nr. of wheels w(i)
yes => w(i) = 4
no => w(i) = 2
Total RRC calculation
m [kg] = total vehicle weight
g [m/s²] = 9.81
β [-] = 0.9

## Slide 13
File Signing
File signing ensures that...
result files were actually created by VECTO and not modified afterwards
files were not changed after signing
specific input files were used for calculation
a file's origin (license owner) is traceable

## Slide 14
File Signing
After each calculation a signature file (.vsig) is created which includes signatures for all input and result files. The file itself is also signed.
Signature files can be verified or manually created under "Tools" > "Sign or Verify Files"
When verifying it can be checked if the file was automatically or user-created. (Automatically created files include input and result file signatures.)

## Slide 15: Full Changelog V1.4 (1/3)
VECTO 1.4
Bugfix: FC interpolation failed when load points matched map points exactly.
Bugfix: Invalid "FC= -10000!" errors when outside of FC-Map
Bugfix: Vehicle stand-still at end of cycle was ignored (distance-based cycles only)
Bugfix: Distance Correction didn't work right with Look Ahead Coasting. Now distance error is acceptable but at the cost of partly interrupted coasting phases. Should be revised in future updates.
FC extrapolation will not abort calculation. Invalid FC values are marked in output as "ERROR".
No abortion if transmission output and input torque have different signs (In>0, Out<0). (Caused "Transmission Loss Map invalid" error messages)
Eco-Roll revised. New rules:
  Engages if Pwheel < 0
  Disengages if Underspeed is reached.
Look-Ahead Coasting now uses real coasting also if road gradient > 0 which means the coasting deceleration can be so high that no braking is necessary. In this case the braking phase will be omitted and the total deceleration time can be shorter than expected by the given target coasting deceleration.
"Minimum (actual) speed" instead of "Min. Target Speed" for Eco-Roll, Overspeed and Look Ahead Coasting
Load-dependent rolling resistance coefficient

## Slide 16: Full Changelog V1.4 (2/3)
VECTO 1.4 (cont.)
Major update in Gearbox/Toque Converter:
  Torque converter can be defined in multiple gears
  Same gear numbers in output as in GBX file, i.e. first gear with TC is not "TC" or "0.5" but simply "1"
  "Minimum time between two gear shifts" now also limits torque converter shifts
  Unlimited number of gears and new gear list in GUI without fixed gear number
  Improved gear shift model for torque converter
  Driving Cycle Pre-processing and Gear Shift Model now use approximated efficiency values based in the transmission loss maps. Reduces calculation time significantly with little to no impact on fuel consumption.
Full load and drag curves (.vfld) can be defined for each gear separately.
Engine Only Mode: Engine motoring points can be defined explicitly in load cycle with "<DRAG>"
When speed is under 5km/h and engine in motoring operating then gearbox shifts to Neutral
Start-Stop activation delay time can be defined in job file
File signing features added:
  After each calculation a signature file (.vsig) is created which includes signatures for all input and result files. The file itself is also signed.
  Signature files can be verified or manually created under "Tools" > "Sign or Verify Files"

## Slide 17: Full Changelog V1.4 (3/3)
VECTO 1.4 (cont.)
Changes in header and new parameters in modal results (.vmod):
  engine speed => n
  torque => Tq_eng
  Pe => Pe_eng
  New: Tq_clutch = torque at clutch (before clutch, engine-side)
  New: Tq_full = full load torque
  New: Tq_drag = drag torque
  Removed: Pe_norm, n_norm
Changes in summary results (.vsum)
  Total altitude change instead of average gradient
  Auxiliary energy consumption for each auxiliary
  Removed: Pe_norm, n_norm
Same job file list for BATCH and STANDARD (Job file list does not change when switching mode)
Updated some error messages (units)
Driving Cycle stop times corrected (No more zero stop times).

## Slide 18
VECTO 1.3.1
16.05.2013
Update Notes

## Slide 19
VECTO 1.3.1
Update Overview (since V1.0):
Driver Model:
  Overspeed
  Eco-Roll
  Look Ahead Coasting
New Gear Shift Model
  Shifting based on used-defined shift polygons
  Sequential shifting or gear skipping
  Optional shifting inside polygons
  Start gear calculation
Torque Converter Calculation
Engine Only Mode
Engine Start/Stop
Visualizer (GRAPHi)
User Manual updated with function descriptions
Error messages linked to user manual
Demo Data updated

## Slide 20: Driver Model
Overview:
Overspeed
  If Pwheel < 0: Coasting with brakes not applied for speed < target speed + allowed overspeed
Eco-Roll
  If Pwheel < 0: Neutral gear, engine idling.
  Engine and service brake if target speed + allowed overspeed is reached.
  Normal driving if target speed + allowed underspeed is reached.
Look Ahead Coasting
  Phase of coasting put in front of braking phases

## Slide 21: VECTO Editor - Driver Tab
Overspeed:
Functionality:
  If Pwheel < 0: Coasting with brakes not applied for speed < target speed + allowed overspeed
Parameters:
  Minimum Target Speed, e.g. 70km/h
  Allowed Overspeed, e.g. 5km/h

## Slide 22: VECTO Editor - Driver Tab
Eco-Roll:
Functionality:
  If Pwheel < 0: Neutral gear, engine idling.
  Engine and service brake if target speed + allowed overspeed is reached.
  Normal driving if target speed + allowed underspeed is reached.
Parameters:
  Minimum Target Speed, e.g. 70km/h
  Allowed Overspeed, e.g. 5km/h
  Allowed Underspeed, e.g. 5km/h

## Slide 23: VECTO Editor - Driver Tab
Look-Ahead Coasting:
Functionality:
  Phase of coasting put in front of braking phases
Parameters:
  Reference (target) deceleration,
  e.g. -0.5m/s²
  Minimum speed, e.g. 55km/h (e.g. might be used for citybus driving)

## Slide 24
VECTO 1.2
09.04.2013
Update Notes

## Slide 25: Gearbox updates
Overview:
Default settings for each transmission type
Torque Converter implemented
(Shift Polygons are described in the 1.1 beta Update Notes attached below)

## Slide 26: Gearbox updates
Transmission Type:
Manual Transmission (MT):
  Activates the "Skip Gears" option. No torque converter.
Automated Manual Transmission (AMT)
  Activates the "Allow shift-up inside polygons" and "Skip Gears" option. No torque converter.
Automatic Transmission (AT)
  Torque converter ist set and must be parameterized.
Custom
  Enables all options for user-defined settings.

## Slide 27: Gearbox updates
Torque Converter (TC):
"Installed" can only be changed if Transmission Type is "Custom"
The torque converter is only used in the first gear (TC), i.e. the lock-up clutch is open. After TC comes gear 1(first gear with closed lock-up clutch).

## Slide 28: Gearbox updates
Torque Converter characteristics file (.vtcc):
Defines:
  torque ratio (= Output Torque / Input Torque) and
  input torque at reference engine speed
  over speed ratio (= Output Speed / Input Speed)
Must include data for motoring (speed ratio > 1)!
c Speed Ratio ν | Torque Ratio μ | Input Torque at reference rpm
c [-] | [-] | [Nm]
0 | ... | ...
0.1 |  | 
... | ... | ...
>1! | ... | ...
*VECTO CSV Format:
List Separator: Comma ","
Decimal-Mark: Dot "."
Comments/headers: "c" at the beginning of the comment line. Number and position of comment lines is not limited.

## Slide 29: Gearbox updates
Reference rpm for torque characteristic:
Needed to calculate the actual engine torque
with:
Tin = engine torque [Nm]
Tref(ν) = reference torque at reference rpm (form .vtcc file) [Nm]
nin = engine speed [1/min]
nref = reference rpm (from .vgbx file) [1/min]
Calculation of engine torque (if lock-up clutch is open, gear "TC"):

## Slide 30: Torque Converter Calculation
Engine
Same polygon-based gear shift model as MT/AMT
Torque Converter (TC):
  Defined as (virtual) separate gear, i.e. only first gear with TC active
  While TC active: Iterative calculation of engine torque and speed based on TC characteristic
  Creeping: Engine speed set to idling. Brakes engaged to absorb surplus torque
Longitudinal dynamics
Transmission losses added
Quasi stationary backwards calculation
Iteration
Torque converter
Transmission
Torque converter characteristic (.vtcc file)

## Slide 31: Engine Only Mode (.vecto file)
Calculate fuel consumption using a predefined load cycle
No gearbox, vehicle or Aux file required
Cycle format (see User Manual):
  engine speed <n> [1/min]
  engine power <Pe> [kW]
      or
  engine torque <Me> [Nm]
  [Optional] Additional power demand (aux) <Padd>
Engine inertia (from .veng file) is added to the input torque!

## Slide 32: Engine Start / Stop (.vecto file)
Engine will be turned off if:
  Power demand (without Aux) ≤ 0
  Vehicle speed is below "Max speed [km/h]"
  Engine was running for at least "Min ICE-On Time [s]"
TBD: Invalid auxiliary consumption work over cycle

## Slide 33: New "Open file" button
Opens a menu with three options:
Open with GRAPHi (see next slide)
Open with user-defined tool (see Settings)
Show in Folder (opens explorer)

## Slide 34: Visualizer (GRAPHi)
Independent 2D visualisation tool (see "GRAPHi" subfolder)
Supports CSV and MS Excel files
User Manual included ("?" button)
Located in "GRAPHi" subfolder
Note: GRAPHi is not a permanent part of VECTO and will be provided by TUG for a limited time only

## Slide 35: GRAPHi Quick Start (1/5)
Use the "+" Button to add files (excel or csv)
Opening files
Once a file is loaded, it remains in memory without accessing the file on the hard drive (unless manually reloaded).

## Slide 36: GRAPHi Quick Start (2/5)
Move
Zoom
[Drag&Drop]
Hold cursor over x-axis to zoom/move x-axis only!!!
Zoom-Box
Click 1: 1st corner
Click 2: 2nd corner
(Right-Click to Cancel)
Mouse Controls

## Slide 37: GRAPHi Quick Start (3/5)
Save/Load Session (.GRAPHi file)
Opening and Saving Sessions
Session files (.GRAPHi) include all data to restore a session. Source files are saved only as reference, i.e. the original files must be accessable.

## Slide 38: GRAPHi Quick Start (4/5)
Add Window
Sync open windows (x-axis, left and right y-axis)
Windows and Syncing
Syncing means changes to the synced axes in one window are reflected by all other windows which have the same axes synced.

## Slide 39: GRAPHi Quick Start (5/5)
The User Manual can be opened here
User Manual

## Slide 40: Full Changelog V1.2
VECTO 1.2
Engine Start/Stop implemented
Bugfix: Fixed error in FC interpolation (invalid extrapolation errors)
FC Extrapolation will abort the calculation
Transmission Type selection in Gearbox (.vgbx) file.
  Enables/Disables transmission type-specific options
  In Proof-Of-Concept mode "Custom" type is available with all options enabled.
Automatic Transmission mode with Torque converter: Input parameters in Gearbox file !!still being tested!!
Option to open files with GRAPHi or user-defined tool
User Manual updated
Bugfix: Files with relative paths were not located correctly
Corrected comment line for wheels inertia and axle config in .vveh file
Changed RRC unit in GUI from [-] to [N/N]
Tranmission Loss Maps are not converted to n,Pe-Maps anymore. Should fix non-linear interpolation effects.
Engine Only Mode

## Slide 41
VECTO 1.1 beta
05.02.2013
Update Notes

## Slide 42: New gear shift model for MT and AMT
Overview:
Shifting based on used-defined shift polygons
Sequential shifting or gear skipping
Optional shifting inside polygons
Customisable start gear calculation

## Slide 43: New parameters in .vgbx file
Shift polygons file:
CSV file* defining up- and downshift rpms over torque
File must cover full engine range including motoring
Two or more rows required
Upshift
Down-
shift
c Torque | Downshift | Upshift
c [Nm] | [rpm] | [rpm]
-500 | 650 | 900
0 | 650 | 900
500 | 700 | 950
... | ... | ...
*VECTO CSV Format:
List Separator: Comma ","
Decimal-Mark: Dot "."
Comments/headers: "c" at the beginning of the comment line. Number and position of comment lines is not limited.

## Slide 44: New parameters in .vgbx file
Allow shift-up inside polygons (AMT):
Only if torque reserve is provided and rpm is still above Down-shift-rpm
Upshift
Down-
shift
Min % from max. positive torque at actual engine speed

## Slide 45: New parameters in .vgbx file
Skip gears (AMT, MT):
Whenever gear shift is initiated (because rpm crosses up- or down- shift polygon) it is possible to skip gears
Torque reserve must be provided and rpm must remain below Down-shift-rpm
Upshift
Down-
shift
Min % from max. positive torque at actual engine speed

## Slide 46: New parameters in .vgbx file
Minimum time between two gear shifts:
Limits the time between two gear shifts in whole seconds
Rule will be ignored if rpms are too high/low
High values may cause high rpms during acceleration

## Slide 47: New parameters in .vgbx file
Start gear (first gear after vehicle standstill):
Calculated using a fictional load case with:
  Reference speed
  Reference acceleration
  Actual road gradient, transm. losses and aux. power demand
uphill
downhill
independent from target speed
Example: Half-loaded articulated truck, 80km/h target speed:

## Slide 48: Important notes
The demo data is updated for VECTO 1.1 and ready to run with the new gear shift model
Format of .vecto files has changed:
  Old .vecto files (V1.0) can be used with VECTO 1.1.
  New .vecto files (V1.1) can NOT be used with VECTO 1.0.
Format of .vgbx files has changed:
  Old .vgbx files (V1.0) can be opened in the gearbox editor but gear shift parameters must be set before starting calculation.
  New .vgbx files (V1.1) can be used with VECTO 1.0 but saving files will remove the new parameters.
The old gear shift model is NOT available in VECTO 1.1.
The User Manual and Quick Start Guide do not cover the new gear shift model yet.

## Slide 49: Full Changelog V1.1 beta
VECTO 1.1 beta
- Speed values below 0.09km/h are set to 0km/h
- New gear shift model
- Replaces old gear shift model!
- New parameters in .vgbx file including path to gear shift polygons file
- Old gear shift model parameters removed from .vecto file
- Command Line Arguments processing (see User Manual):
- Changed prefix form "/" to "-"
- Bugfix: Argument "-run" was not processed
- Job files and driving cycles can be added via command line
- Files without path are expected in the Working Directory
- User Manual update for command line arguments
- Various fixes in GUI
- Bugfix: Error in Cycle Conversion (distance- to time-based) when using Aux Power Input.
- Distance Correction is now active only in acceleration and cruise phases.
- Fixed cycles starting with vehicle speed = 0. In V1.0 the first and second time step were averaged to speed values > 0.
- Demo data updated for new gear shift model
- New independent licensing dll replaces TUG's version